Table 3.  Comparison of Setback Requirements for Private Wells

| Setback From (in Feet) | Acton | Boxborough | Burlington | Carlisle | Charlton | Groton | Harvard | Lexington | Littleton | Lunenberg | Northbridge | Pepperell | Stow | Sudbury | Westford | State Recommended |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Leaching Facility | 100 | 100 | 100 |  | 100 | 100 | 100 | 150 | 100 | 100 | 100 | 100 | 150 | 100/150 | 100 | 100 |
| Leaching facility <2 mpi |  |  |  |  |  |  | 125 |  | 150 |  |  |  |  |  |  |  |
| Cesspool |  |  |  |  | 100 | 100 | 100 |  | 100 | 100 | 100 | 100 | 100 |  |  |  |
| Distribution Box |  |  |  |  |  |  |  | 75 |  |  |  |  |  |  |  |  |
| Septic Tank |  |  | 50 |  | 50 | 50 | 50 | 75 | 50 | 50 | 50 | 50 | 100 |  | 100 |  |
| Sewer Line |  |  | 10/50 |  | 50 | 50 | 50 | 50 | 50 | 50 | 10/50 | 20 | 50 |  |  |  |
| Property Line |  | 10 | 10 | 25 | 10 | 50 | 25 |  | 50 | 50 | 10 | 20 | 25 |  | 50 | 10 |
| Public or private way or common drive easement | 25 | 35 | 25 | 25 | 25 | 75 | 25 | 25 | 50 | 50 | 25 | 20 | 25 | 75 |  | 25 |
| Active or closed landfill |  | 400 |  |  |  | 400 | 400 |  | 400 | 400 | 1000 |  | 400 |  |  |  |
| Hazardous Waste Spill Site |  | 400 |  |  |  | 400 | 400 |  | 400 | 400 |  |  | 400 |  |  |  |
| Any type of surface water |  |  | 25 |  | 25/ 100 | 100 | 50 |  | 100 |  |  |  | 100 |  |  |  |
| Storm drains |  |  |  |  |  |  |  |  |  |  | 25 |  | 25 |  |  |  |
| Dwelling unit, incl. overhang |  |  |  |  |  |  |  |  |  |  |  |  | 25 |  |  |  |
| Building/Structure |  |  | 5 |  | 20 |  |  |  |  |  | 20 | 20 |  |  |  |  |
| Driveway |  |  |  |  | 10 |  |  | 25 |  |  | 25 | 20 |  |  |  |  |
| Right of way |  |  |  |  | 10 |  |  | 50 |  |  | 15 |  |  |  |  |  |
| Stable/manure storage |  |  |  |  |  |  |  |  |  |  | 100 |  |  |  |  |  |
| Underground storage tank |  |  |  |  |  |  |  |  |  |  | 200 |  | 200 |  |  |  |
| Wetland |  |  |  |  |  |  |  |  |  |  | 50 | 50 |  |  | 25 |  |
| Irrigation Well |  |  |  |  |  |  | 50 |  |  |  |  |  |  |  |  |  |
| Subsurface drains |  |  |  |  |  |  |  | 25 |  |  |  |  |  |  |  |  |

# Footnotes

Sudbury:  150 feet if perc rate < 3mpi.  Other setbacks according to Title 5 except “All distances shall be increased where required by conditions peculiar to a location or by other Town Regulations or By-Laws.”

Burlington and Northbridge setback = “10 feet from building sewer constructed of durable corrosion resistant material with watertight joints, or 50 feet from…any other type.”

Setback from street only

From center of road

1000 foot setback from any Waste Disposal Site/Landfill

25 feet for drilled well, 100 feet for dug well